Technical data sheet

Le ORIGINI

sez. 1.0 Technical Characteristcs

Origini is a versatile paint that can meet the different needs of aesthetics, durability and washability thanks to our wax. A stylish finishing with a soft touch, with a matt or slightly glossy effect, or even stained, which conveys the beauty of something born in nature with an endless fascination.

sez. 2.0 Use

Origini is suitable for decorating indoor wall surfaces..

sez. 3.0 Preparing the surface

Preparing the wall is vital to the success of the coating. It is therefore advisable to trim and insulate properly before use, and to apply Primus Sabbia (as specified in the application method), which guarantee optimal grip and absorbency of the product.

sez. 4.0 Application method

Apply Primus Sabbia in 2 coats by roller. Origini is not ready to use: after introducing the quantity of COLOURING AGENT specified in the catalogue, add 20% water, up to 30% if needed, and then mix well until the shade obtained is completely even. The product can be applied in 2 coats by brush. First Coat: Apply the product by brush stretching and blending. Second Coat: after 8 hours apply the second coat, stretching and blending. If you want to realize a satinated/glossy effect, once the second coat has dried, it’s enough to stroke the wall with a big clean brush or with a cotton cloth. If you want to realize a stained effect, stroke the wall with a clean brush before the wall is dried, so as to create stains on the still wet areas.

sez. 5 Protective finish

Cera del vecchio: after the wall has dried, at least after 24 hours, apply the wax with a sponge, well stretching. After 5/10 minutes, pass on again with a cotton cloth, as to increase slightly the satinated effect. The finishing with Cera del Vecchio allows the washability of the wall.

sez. 6.0 Technical characteristics: application

| Dilution/Mixing | Diluition with 20/30 % water before to use |
| --- | --- |
| Consumption | 8 mq/l with diluition of 20% |
| Tools for application | Brush |
| Primus | Primus Sabbia |
| Protective coating | Cera del vecchio |
| Application temperature | The ambient temperature must not be less than +5° C. Do not apply onto hot surfaces or those exposed to sunlight. |
| Drying time | The drying time varies between 6 and 8 hours |

sez. 7.0 Technical characteristics: the product

| Composition | Slaked lime, water |
| --- | --- |
| Specific weight | 1.29 Kg/l |
| pH after 30 days | > 12,5 |
| Viscosity | > 6600 mPas (Brookfield, sonda n 3 , 10rpm 20° C)) |
| Storage temperature | Store in a sealed pot at a temperature of more than +5° C. Keep away from extreme cold. |
| EU VOC limit value for this product (cat. A/I): 300 g/l (2007) 200 g/l (2010) | Max content VOC 2 g/l white |
| Colours available | As per our catalogue |
| Pot sizes | Lt 1 – 2,5 – 5 |
| Warnings | If inhaled: Take the patient to a well ventilated location. Contact with eyes: rinse immediately with plenty of running water for at least 10 minutes. Skin contact: wash with running water; avoid prolonged contact. |